Chapter 11:-Dynamic Host Configuration Protocol (DHCP)

Dynamic Host Configuration Protocol (DHCP)
The Dynamic Host Configuration Protocol (DHCP) is a network service that enables host computers to be automatically assigned settings from a server as opposed to manually configuring each network host. Computers configured to be DHCP clients have no control over the settings they receive from the DHCP server, and the configuration is transparent to the computer's user.
The most common settings provided by a DHCP server to DHCP clients include:
- IP address and netmask
- IP address of the default-gateway to use
- IP adresses of the DNS servers to use
However, a DHCP server can also supply configuration properties such as:
- Host Name
- Domain Name
- Time Server
- Print Server
The advantage of using DHCP is that changes to the network, for example a change in the address of the DNS server, need only be changed at the DHCP server, and all network hosts will be reconfigured the next time their DHCP clients poll the DHCP server. As an added advantage, it is also easier to integrate new computers into the network, as there is no need to check for the availability of an IP address. Conflicts in IP address allocation are also reduced.
A DHCP server can provide configuration settings using the following methods:
Manual allocation (MAC address)
This method entails using DHCP to identify the unique hardware address of each network card connected to the network and then continually supplying a constant configuration each time the DHCP client makes a request to the DHCP server using that network device. This ensures that a particular address is assigned automatically to that network card, based on it's MAC address.
Dynamic allocation (address pool)
In this method, the DHCP server will assign an IP address from a pool of addresses (sometimes also called a range or scope) for a period of time or lease, that is configured on the server or until the client informs the server that it doesn't need the address anymore. This way, the clients will be receiving their configuration properties dynamically and on a "first come, first served" basis. When a DHCP client is no longer on the network for a specified period, the configuration is expired and released back to the address pool for use by other DHCP Clients. This way, an address can be leased or used for a period of time. After this period, the client has to renegociate the lease with the server to maintain use of the address.
Automatic allocation
Using this method, the DHCP automatically assigns an IP address permanently to a device, selecting it from a pool of available addresses. Usually DHCP is used to assign a temporary address to a client, but a DHCP server can allow an infinite lease time.
The last two methods can be considered "automatic" because in each case the DHCP server assigns an address with no extra intervention needed. The only difference between them is in how long the IP address is leased, in other words whether a client's address varies over time. Ubuntu is shipped with both DHCP server and client. The server is dhcpd (dynamic host configuration protocol daemon). The client provided with Ubuntu is dhclient and should be installed on all computers required to be automatically configured. Both programs are easy to install and configure and will be automatically started at system boot.
- Installation
- Configuration
- References
Installation
At a terminal prompt, enter the following command to install dhcpd:
sudo apt install isc-dhcp-server
You will probably need to change the default configuration by editing /etc/dhcp/dhcpd.conf to suit your needs and particular configuration.
You also may need to edit /etc/default/isc-dhcp-server to specify the interfaces dhcpd should listen to.
NOTE: dhcpd's messages are being sent to syslog. Look there for diagnostics messages.
Configuration
The error message the installation ends with might be a little confusing, but the following steps will help you configure the service:
Most commonly, what you want to do is assign an IP address randomly. This can be done with settings as follows:
# minimal sample /etc/dhcp/dhcpd.conf
default-lease-time 600;
max-lease-time 7200;

subnet 192.168.1.0 netmask 255.255.255.0 {
 range 192.168.1.150 192.168.1.200;
 option routers 192.168.1.254;
 option domain-name-servers 192.168.1.1, 192.168.1.2;
 option domain-name "mydomain.example";
}
This will result in the DHCP server giving clients an IP address from the range 192.168.1.150-192.168.1.200. It will lease an IP address for 600 seconds if the client doesn't ask for a specific time frame. Otherwise the maximum (allowed) lease will be 7200 seconds. The server will also "advise" the client to use 192.168.1.254 as the default-gateway and 192.168.1.1 and 192.168.1.2 as its DNS servers.
After changing the config file you have to restart the dhcpd:
sudo systemctl restart isc-dhcp-server.service

What is DHCP?
Anyone with a basic knowledge of computer networking knows that for two hosts to communicate on the same network using TCP/IP model, both hosts need to have a unique IP address. There are two ways on how any given host on your network can obtain an IP address.
One way is to manually configure the network interface and assign an IP address by hand. The manual network configuration is called static configuration, which means that host's IP address does not change its IP address unless changed manually by the user or system administrator. If your company network includes more than 1000 hosts, the job of configuring each host with a static IP address becomes tiresome and more importantly extremely inefficient.
Another way to assign your network hosts with a proper IP address regardless of the actual network size is to assign an IP address to each host automatically. To perform an automatic host's IP configuration is where DHCP ( Dynamic Host Configuration Protocol ) comes handy.
The DHCP protocol lets a DHCP client, that is your network host to lease network configuration parameters such as an IP address. In fact, lease parameters are not limited to IP address only as they may also include the following configuration settings:
- IP addresses and network masks
- Domain Names servers ( DNS )
- Default Gateways
- WINS servers
- Syslog hosts
- Proxy servers
- NTP servers
- X Font servers
- Syslog hosts
Each network host configured to obtain an IP address dynamically via DHCP will upon boot send a DHCP request over the network ( by definition this is a broadcast of all 1's ) to discover whether there is a DHCP server available somewhere on the network and consequently ask for a network configuration. DHCP client is then obligated to maintain communication with DHCP server and renew its IP address regularly as dictated by IP address's lease time expiry. In case that DHCP client fails to renew its IP address ( disconnection, a host is turned off, etc. ) its IP address expires and DHCP server is free to lease this IP address to another DHCP client.
DHCP server keeps a record of all leased IP addresses and stores them in a file called dhcpd.leases within /var/lib/dhcp directory ( location of this file may vary depending on Linux system in use ). Having such a file allows DHCP server to keep track of all IP address leases even after the reboot or power failure.
Here are some advantages of having a DHCP server connected to network:
- No IP address conflicts. DHCP can guarantee that all hosts on the network have a unique IP address. DHCP server keeps a record of all IP addresses assigned and cross reference them with host's MAC addresses.
- Based on the MAC address, DHCP allows for a fixed parameter configuration for a specific host
- minimum local client network configuration, hence Increased efficiency

DHCP Server Installation
Standard DHCP server implementation available in various Linux distributions is an Open source version maintained by ISC ( Internet System Consortium ).
Use the following commands to install DHCP on your Linux server:
Debian and Ubuntu:
# apt-get install isc-dhcp-server
Redhat & Fedora:
# yum install dhcp
Basic DHCP Configuration
By default, DHCP server configuration does not include any subnets on which DHCP server should lease IP addresses. Therefore, depends on your Linux system you may get the following error message when you attempt to start DHCP with default dhcpd.conf configuration file.
Starting ISC DHCP server: dhcpdcheck syslog for diagnostics. ... failed!
Examining log files such as /var/log/syslog reveals more details:
No subnet declaration for eth0 (some IP address).
Your server may be connected to multiple network subnets. To start DHCP server, at least one subnet must be defined within the DHCP configuration file /etc/dhcp/dhcpd.conf.
NOTE: if your server has access to more than one subnet, DHCP requires all subnets to be defined even though there isn't immediate intention to enable DHCP service on that subnet.
Below is the simplest example of DHCP configuration file:
subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
}

subnet 192.168.0.0 netmask 255.255.0.0 {
}
This configuration file instructs DHCP server to listen for DHCP client requests on subnet 10.1.1.0 with netmask 255.255.255.0. Furthermore, it will assign IP addresses in range 10.1.1.3 - 10.1.1.254. It also defines an empty definition for subnet with network ID 192.168.0.0.
Alter the above code with your subnet and insert it into /etc/dhcp/dhcpd.conf. When ready, restart your DHCP server with ( restart command may vary ) :
# service isc-dhcp-server restart

DHCP default and max lease time
At this point we can add feww aditional settings to our DHCP configuration, namely the default and max lease time expiry.
- default-lease-time is a value in seconds in which a leased IP address expiry will be set to if DHCP client does not ask for any other specific expiry lease time
- max-lease-time is a value in seconds which defines a maximum expiry time for an IP address leased by DHCP server
default-lease-time 600;
max-lease-time 7200;

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
}

subnet 192.168.0.0 netmask 255.255.0.0 {
}

Define DNS server
Another configuration parameter possible to be set by DHCP server to its client is a definition of DNS server. If you want your clients to use DNS server with an IP address 8.8.8.8 and 10.1.1.1 you can do it by including an option "domain-name-servers" to DHCP's configuration file.
default-lease-time 600;
max-lease-time 7200;

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
  option domain-name-servers 10.1.1.1, 8.8.8.8;
}

subnet 192.168.0.0 netmask 255.255.0.0 {
}

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
  option routers 10.1.1.1;
}

Set default gateway
DHCP also allows for client's gateway configuration.To set any client on the local network to use default gateway 10.1.1.1, add line "option routers 10.1.1.1" into dhcpd.conf file as demonstrated below:
default-lease-time 600;
max-lease-time 7200;

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
  option domain-name-servers 10.1.1.1, 8.8.8.8;
  option routers 10.1.1.1;
}

subnet 192.168.0.0 netmask 255.255.0.0 {
}

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
  option routers 10.1.1.1;
}
DHCP will now set DHCP client with gateway 10.1.1.1.

Host specific configuration
There maybe a need to set static IP address to a particular host on the network such as printer, web server and etc. In this case it is posible to amend DHCP server configuration to lease a choosen IP address to a specific host defined by its MAC address.
default-lease-time 600;
max-lease-time 7200;

subnet 10.1.1.0 netmask 255.255.255.0 {
  range 10.1.1.3 10.1.1.254;
  option domain-name-servers 10.1.1.1, 8.8.8.8;
  option routers 10.1.1.1;
}

subnet 192.168.0.0 netmask 255.255.0.0 {
}

host printer {
  hardware ethernet 00:16:d3:b7:8f:86;
  fixed-address 10.1.1.100;
}

host web-server {
  hardware ethernet 00:17:a4:c2:44:22;
  fixed-address 10.1.1.200;
}
The above DHCP configuration file will permanently assign the IP address 10.1.1.100 to a host "printer" with a MAC address 00:16:d3:b7:8f:86 and IP address 10.1.1.200 to host "web-server" with MAC address 00:17:a4:c2:44:22.
Appendix
Ubuntu client network settings to use DHCP
To configure your client to use a DHCP on a network interface eth0 on Ubuntu or Debian linux systems enter a following lines in your /etc/network/interfaces file:
auto eth0
iface eth0 inet dhcp
Configuring DHCP relay agent
If your DHCP server does not have an access to some particular subnet it does not mean that it cannot provide its services there. To make this work a DHCP relay agent needs to be configured on a remote subnet which forwards all request to a specified DHCP server and distant subnet. First install DHCP relay agent:
# apt-get install isc-dhcp-relay
Then create a configuration file /etc/default/isc-dhcp-relay with two lines:
SERVERS="192.168.5.5"
INTERFACES="eth0"
The above config file will instruct DHCP relay agent to listen on eth0 interface for a DHCP client requests and forward them to a DHCP server on an IP address 192.168.5.5.