## Slide 1
RAID (Redundant Array Of InExpensive Disks)
RAID is an acronym for Redundant Array of Independent (or Inexpensive) Disks. In fact, RAID is the way of combining several independent and relatively small disks into a single storage of a large size. The disks included into the array are called array members. The disks can be combined into the array in different ways which are known as RAID levels.
Each of RAID levels has its own characteristics.
Fault-tolerance which is the ability to survive of one or several disk failures.
Performance which shows the change in the read and write speed of the entire array as compared to a single disk.
The capacity of the array which is determined by the amount of user data that can be written to the array. The array capacity depends on the RAID level and does not always match the sum of the sizes of the RAID member disks.

## Slide 2
RAID 0 - based on striping. This RAID level doesn't provide fault tolerance but increases the system performance (high read and write speed).
RAID 1 - utilizes mirroring technique, increases read speed in some cases, and provides fault tolerance in the loss of no more than one member disk.
RAID 0+1 - based on the combination of striping and mirroring techniques. This RAID level inherits RAID 0 performance and RAID 1 fault tolerance.
RAID1E - uses both striping and mirroring techniques, can survive a failure of one member disk or any number of nonadjacent disks. There are three subtypes of RAID 1E layout: near, interleaved, and far.
RAID 5 - utilizes both striping and parity techniques. Provides the read speed improvement as in RAID 0 approximately, survives the loss of one RAID member disk.
RAID 5E - a variation of RAID 5 layout the only difference of which is an integrated spare space allowing to rebuild a failed array immediately in case of a disk failure.
RAID 5 with delayed parity - pretty similar to basic RAID 5 layout, but uses nonstandard scheme of striping.
RAID 6 - similar to RAID 5 but uses two different parity functions. The read speed is the same as in RAID 5.
RAID levels :-

## Slide 3
RAID can be created by two different ways:
  Software RAID.
  Hardware RAID.
RAID implementations :-